## Slide 1: LEGO ELEVATOR
Ambrus Bence tibor, d1o4nv

## Slide 2: Concept
lego elevator
The idea was to build an elevator using:
  LEGO
  Arduino UNO
  DC or stepper motor
  motor driver circuit
  some electrical components

## Slide 3: ARDUINO UNO R3 / DUEMILANOVE
lego elevator
I have both of them, they are almost fully identical.
Decided to use Duemilanove because UNO wasn’t recognizedby my girlfriend’s Macbook.
This is a cheap and very widely used and supported microcontroller
It has digital and analog I/O ports that are easy to configure.
The soul of it is a 16.000 MHz crystal.

## Slide 4: Things I’ve tried
lego elevator

## Slide 5: driver
lego elevator
Originally used an L298N:
  has PWM
Replaced with L9110:
  no PWM
  Arduino has PWM output
  smaller

## Slide 6: Electric Technic Motor 9V
lego elevator
ungeared
high speed
low torque
strong enough to lift cabin
gear reduction was needed

## Slide 7: overall picture
lego elevator

## Slide 8: before - after
lego elevator

## Slide 9: before - after
lego elevator

## Slide 10: elevator
lego elevator
3-storey-tall
made of Technics elements
used thread but it always tears
replaced with fishing line (damil)
no horizontal swinging

## Slide 11: control unit
lego elevator
early stage
can move up and down
manual working
cannot be called from levels

## Slide 12: Final stage
Lego elevator

## Slide 13: Overall picture
Lego elevator
The elevator functions as desired.
It has 4 levels.
All 3 requirements have been fulfilled.
Bit slow but punctual.

## Slide 14: The control panel
Lego elevator
Consists of:
  4 level calling buttons
  Up and down buttons
  7 segment display (with shift register below)
  Red LED indicating going up
  Green LED indicating going down

## Slide 15: 7 segment display
Lego elevator
This is a common cathode display with red LEDs built in
Shift register is a 74HC595N by Texas Instruments
It took a while to understand the working and controlling principles of the display but it was interesting to learn it.
Some soldering was needed to save some space on the board

## Slide 16: Stepper motor
Lego elevator
28BYJ-48 stepper motor is used
Works with 5V
Number of phases: 4
Torque: 4.3mN.m
Resolution: 5.625°
It has 4096 steps resolution
The motor has 360/5.625 = 64 steps/rev, but the output shaft has 64 steps/rev * 32 gear ratio = 2048 steps/rev, or 0.17°/step
I use full stepping mode, it gives more torque

## Slide 17: Driver circuit
Lego elevator
ULN2003 is used
It is quite trivial how to connect to the motor and to the microcontroller as well
4 LEDs show which coils are active at the moment (in my case it’s way too fast)

## Slide 18: Difference between half and full stepping
Lego elevator

## Slide 19: Pictures
Lego elevator

## Slide 20: For next semester
Lego elevator
Multiple level calls handling
UP/DOWN calling buttons on each levels
Emergency stop
Use sensors to identify actual level
Connect to a server to send usage data
Remote control
Servo controlled doors

## Slide 21: End of presentation
Lego elevator
Thank you very much for
your attention!